## Slide 1: EE 564 Design of Electrical Machines
Fault-tolerant electric machines
Mustafa ÇELİKKAYA

## Slide 2: Outline
Definitions
History
Application Areas
Fault Types
Fault Type Approaches
  Geometry
  Winding
Motor Drive System Failures and Solutions
Thermal Protection
Conclusion
References

## Slide 3: What is Fault-Tolerant ?
The machine needs to maintain the same or comparable performance under fault to that when the machine was healthy.
In case of fault, the machine needs to fail safe without any catastrophic damage. (for safety-critical applications)

## Slide 4
A safety critical system is the system whose failure may cause injury or death, which should have the ability to respond to an unexpected hardware or software failure.
A system is reliable when it is capable of operating without material error, fault or failure during a specified period in a specified environment.
A system is dependable if it is available, reliable, safe and secure.

## Slide 5: History
Emerged for the first time in Information Technology.
The necessity of operating a system in degraded mode under the presence of almost any fault.
First Fault Tolerant Drives in early 1990s.
  Jahns, T.M., No.3, May 1980
  Salmon J.C. and Williams B.W., January/February 1980
  Jack A.G, Mecrow B.C., AND Haylock J.A., 1995
  Mecrow B.C., Jack A.G., Haylock J.A., and Coles J, 1996

## Slide 6: Application Areas
Aerospace
Military Applications
Medical
Nuclear Power Plants
Transportation
Electric Vehicle Propulsion
The Wind Power Generation

## Slide 7
Fault Types
Electrical
Magnetic
Physical Separation of various phases
Thermal

## Slide 8: Fault Types in The Drive
Winding open-circuit
Winding short-circuit (partial turn to turn or complete)
Inverter switch open-circuit (similar to winding terminal open-circuit)
Inverter switch short-circuit (analogous to winding terminal short-circuit)
Power device failure (either open or short-circuit)
DC bus open or short-circuit
Controller failure
Mechanical bearing failure
Insulation failure

## Slide 9: Fault Tolerant Approaches
Main idea is;

## Slide 10: Fault Tolerant Approaches
Main idea is;
    « Substitute the faulted phase’s contribution by the healthy remaining ones »

## Slide 11: Fault Tolerant Approaches
Geometry Approach

## Slide 12: Geometry Approach
For multi-phase machines, increasing the number of teeth
A fault tolerant switched reluctance machine

## Slide 13: Geometry Approach
For multi-phase machines, increasing the number of teeth
A fault tolerant switched reluctance machine
Lower torque ripple in case of different faults

## Slide 14
With a lower number of teeth
Geometry Approach
The fault tolerant synchronous permanent magnet machine

## Slide 15
With a lower number of teeth
Geometry Approach
The fault tolerant synchronous permanent magnet machine
Simple magnetic circuit
More Complex Winding
High Number of Phase
Complex Winding Plan
Complicated Drive Unit !!!
MMF Harmonics are Consistent
which causes;
Unbalanced Saturation
  Unbearable Torque Ripple

## Slide 16
Armature coils are placed in pairs of slots
The walls of the slots are parallel to
  Themselves
  The wall of the other slot of the same slot pair
Geometry Approach

## Slide 17
Armature coils are placed in pairs of slots
The walls of the slots are parallel to
  Themselves
  The wall of the other slot of the same slot pair
Geometry Approach
  Spacer Tooth exists
    Narrower than main teeth
  Greater magnetic flux linkage between them
  Thus;
        increasing EMF within the coil.

## Slide 18
What if the rotor is passive ??
Previous solution is not applicable !
The solution is ;
Geometry Approach

## Slide 19
What if the rotor is passive ??
Previous solution is not applicable !
The solution is ;
Geometry Approach
make the rotor active by placing a winding
in closed loop around each rotor pole
Similar to a MAGNET
the rotor will generate the force needed for passing over a pole having damaged winding

## Slide 20: Winding Approach
By changing the winding arrangement
There are two solutions
  Independency between the phase
  Dubling the stator poles

## Slide 21: Winding Approach
independency between the phase windings
in order to reduce the effects of winding damages
  high number of coils & a high number of phases
Higher Torque Density
Small Torque Ripple
Complex Drive

## Slide 22: For Motor Drive System
Key terms:

## Slide 23: For Motor Drive System
Key terms:
Redundancy is a mixture of series or parallel modules.

## Slide 24: For Motor Drive System
Key terms:
Redundancy is a mixture of series or parallel modules.
Reliability is a measure of the time between failures occurring in a system.
  by having alternative backup systems
  By dividing some sections of hardware into small electrically and physically isolated units
    Reliability can be increased.

## Slide 25: For Motor Drive System
The use of direct-drive multiple motors on the SAME shaft
Complexity & Cost increase !
Multiple segment/modular motor drive with redundancy

## Slide 26: For Motor Drive System
Alternative way;
  By separating the 3-phase windings and
  driving each motor phase from a separate
  single-phase inverter
Doubles the number of devices !
However;
Switching losses
Heat sink requirements
  Less room is needed
  Less weight
An alternative motor-inverter configuration

## Slide 27: For Motor Drive System
Alternative way;
  Fourth command branch in standby.

## Slide 28: For Motor Drive System
Alternative way;
  Fourth command branch in standby.
When the fault appears in the machine,
the standby branch becomes active
When the fault appears in the machine,
the standby branch becomes active

## Slide 29: For Motor Drive System
Controlling the fault current value is important when short-circuit failure happens.
In order to limit this current,
        Increase the self-inductance of the windings in design stage.

## Slide 30: For Motor Drive System
Controlling the fault current value is important when short-circuit failure happens.
In order to limit this current,
        Increase the self-inductance (per-unit) of the windings in design stage.

## Slide 31: Thermal Protection
Ferrite material is used in the stator and rotor
In case of fault;

## Slide 32: Thermal Protection
Ferrite material is used in the stator and rotor
In case of fault;
This material heats up due to the high fault current

## Slide 33: Thermal Protection
Ferrite material is used in the stator and rotor
In case of fault;
This material heats up due to the high fault current
Becoming a nonmagnetic material

## Slide 34: Thermal Protection
Ferrite material is used in the stator and rotor
In case of fault;
This material heats up due to the high fault current
Becoming a nonmagnetic material
External heat sources are used to speed up the heating process for cooling the ferrite.

## Slide 35: Conclusion
For geometry and winding approaches,
  Main idea of the solution is substituting the faulted phase’s contribution by the healthy remaining ones. And there are consequences about the dimensions and performances.

## Slide 36: Conclusion
For motor drive systems,
  Higher redundancy, by using identical motor segments on the same shaft
  Electrically isolated phases to prevent phase to phase short-circuit and reduce inverter faults
  Magnetically uncoupled windings to avoid reduction of performance in the case of a failure of the other phases
  Higher winding inductance to limit the winding short-circuit current
  Physically isolated phases to prevent propagation of the fault into the neighboring phases and to increase the thermal isolation
  Effective cooling is important

## Slide 37: References
Operation of Fault Tolerant Machines With Winding Failures, James A. Haylock, Barrie C. Mecrow, Alan G. Jack and David J. Atkinson, IEEE Transactions on Energy Conversion, Vol. 14, No. 4, December 1999
Design and Analysis of a New Fault-Tolerant Permanent-Magnet
Vernier Machine for Electric Vehicles, Guohai Liu, Junqin Yang, Wenxiang Zhao, Jinghua Ji, Qian Chen, and Wensheng Gong, IEEE TRANSACTIONS ON MAGNETICS, VOL. 48, NO. 11, NOVEMBER 2012
Fault Tolerant Electrical Machines State of the Art and Future Directions, Mircea RUBA and Loránd SZABÓ
Fault-Tolerant PM Machines: A Review Ayman M. EL-Refaie, Senior Member IEEE
Fault Tolerant and Minimum Loss Control of Double-Star Synchronous Machines Under Open Phase Conditions, Mohammad-Ali Shamsi-Nejad, Babak Nahid-Mobarakeh, Member, IEEE, Serge Pierfederici, and Farid Meibody-Tabar, IEEE TRANSACTIONS ON INDUSTRIAL ELECTRONICS, VOL. 55, NO. 5, MAY 2008

## Slide 38: References
Optimal Torque Control of Fault-Tolerant Permanent Magnet Brushless Machines, Jiabin Wang, Member, IEEE, Kais Atallah, and David Howe, IEEE TRANSACTIONS ON MAGNETICS, VOL. 39, NO. 5, SEPTEMBER 2003
Fault Tolerant In-Wheel Motor Topologies for High Performance Electric Vehicles, C.J. Ifedi, B.C. Mecrow, S.T.M. Brockway, G.S. Boast, G.J. Atkinson and D. Kostic-Perovic,2011 IEEE IEMDC
Fault Tolerant Motor Drive System with Redundancy for Critical Applications N. Ertugrul, W. Soong, G. Dostal and D. Saxon
Design and Experimental Validation for Direct-Drive Fault-Tolerant Permanent-Magnet Vernier Machines, Guohai Liu, Junqin Yang,Ming Chen, and Qian Chen
Jahns, T.M., "Improved Reliability in Solid State AC Drives by Means of Multiple Independent Phase Drive Units", IEEE Transactions on Industry Applications, Vo1.16, No.3, May 1980, pp. 321-331.
Salmon J.C. and Williams B.W., A Split-Wound Induction Motor Design to Improve the Reliability of PWM Inverter Drives", IEEE Transactions on Industry Applications, Vo1.26, No.1, January/February 1980, pp.143-150.
Mecrow B.C., Jack A.G., Haylock J.A., and Coles J;"Fault Tolerant Permanent Magnet Machine Drives; IEE Proceedings, Electric Power Applications; Volume 143;Number 6; 1996,pp. 437441.
Jack A.G, Mecrow B.C., AND Haylock J.A., " A Comparative Study of Permanent Magnet and Switched Reluctance Motors for High Performance fault Tolerant Applications", IEEE, IAS Annual Meeting, 1995, pp. 734-740.